## Slide 1: Minnesota’s Stormwater Manual – Connecting Stormwater Management to the Landscape
Mike Trojan
Minnesota Pollution Control Agency
Northern Green Expo
January 3, 2018

## Slide 2: Outline
A little bit on stormwater
Overview of the Minnesota Stormwater Manual
History of the Manual
Green Infrastructure and sustainable stormwater management
How the manual is evolving to incorporate sustainable stormwater management

## Slide 3: 1. A little bit on stormwater runoff

## Slide 4: Stormwater Runoff 101
Stormwater runoff is the portion of stormwater that runs off to surface water (lake, river, wetland)
This presentation focuses on urban stormwater runoff, but many of the principles can be applied to agriculture or other settings

## Slide 5: The problem with stormwater runoff
Chart: 
| Agriculture | Hydromodification | Natural causes | Urban runoff | Silviculture | Construction
Percent contribution to waters that are impaired | 29.5 | 6.9 | 3.9 | 3.8 | 2.4 | 1.5
Pollutants in stormwater include sediment, phosphorus, nitrogen, bacteria, organics, metals, and others
The numbers for urban look small, but on a load per area basis they are large
Source: EPA (2005)

## Slide 6: Phosphorus concentrations greater than 40 to 60 ppb typically are problematic for lakes. Typical phosphorus concentrations in runoff are
Less than this concentration
About this concentration
5 times this concentration
10 times this concentration

## Slide 7
Chart: Concentrations in runoff (ppm)
| TSS | Phosphorus (x 100) | Nitrogen (x 10)
Residential | 27 | 33 | 22.9
Commercial | 87 | 29 | 30
Industrial | 94 | 31 | 17.9
Row crop runoff | 55.3 | 34.4 | 23.2
Forested | 11.1 | 5.3 | 5
Source: Lin (2004)

## Slide 8: So we build stormwater best management practices (BMPs) to reduce pollution from stormwater runoff
Bioretention
Vegetated swale
Tree trench
Infiltration basin
Green roof
Permeable pavement
Harvest and reuse
Disconnection

## Slide 9: 2. Overview of the Minnesota Stormwater Manual

## Slide 10: What is the Manual?
A resource that provides guidance and tools to help better manage stormwater

## Slide 11: What is in the Manual?
Guidance on BMP selection
Guidance on BMP implementation
Calculation of pollutant loading
Access to tools
Links and case studies

## Slide 12: Who uses the manual?
Chart: 
| Manager | Engineer | Water specialist | Other technical | Other non-technical | Public works | Planner
% of respondents | 26.8 | 19.1 | 11.7 | 10.5 | 9.3 | 7.8 | 4.7
What’s missing?
About
11 million hits to date

## Slide 13: 3. History of the manual

## Slide 14
1st edition in 2005 by Stormwater Steering Committee
  “a guidance document that could be used as a single source to guide stormwater managers through the maze of regulations, Best Management Practices (BMPs) designs, models/techniques and terminology that constitute good stormwater management”
Minor updates in 2008
Converted to wiki format in 2011
Funding since 2011 to update the content
  Dedicated staff person for Manual upkeep

## Slide 15
1990
2000
1980
2010
2020
Pipes and ponds
Low Impact Development
Better Site Design
Image courtesy of the Capitol Region Watershed District
Green Infrastructure/Sustainable stormwater management
A stormwater timeline

## Slide 16: 4. Green Infrastructure and sustainable stormwater management

## Slide 17: What is sustainable stormwater management?
Managing stormwater in a manner that limits impacts to natural functions of landscapes, hydrologic systems, and habitats (Porter, 2007; Managing Growth in America’s Communities)
  Reuse/replace treated water
  Flood control
  Habitat/biodiversity
  Climate mitigation/adaptation
  Pollutant reduction
  Ecosystem services (e.g. pollination)
  Restore hydrology/recharge groundwater
  Social, economic and other environmental benefits

## Slide 18: Green Infrastructure is the approach used to achieve sustainable stormwater management
Use of stormwater infiltration practices
Harvesting and using stormwater runoff
Disconnecting hard surfaces
Using vegetation
Landscaping
Education
Stormwater Park; Mississippi Watershed Management Organization

## Slide 19: Which of these stormwater practices is generally not considered to be a green infrastructure practice?
Sand filter
Green roof
Constructed wetland
Permeable pavement

## Slide 20: Green Infrastructure stormwater - Best Management Practices (BMPs)
Bioretention
Vegetated swale
Tree trench
Infiltration basin
Green roof
Permeable pavement
Harvest and reuse
Disconnection

## Slide 21: 5. How the manual is evolving to incorporate sustainable stormwater management

## Slide 22: Ways for the Manual to connect to sustainability
Information on the role of stormwater management in green infrastructure and sustainability
Technical guidance and specifications
Tools
Case studies
Links
Communication and outreach

## Slide 23: Information on the role of stormwater management in green infrastructure and sustainability
https://stormwater.pca.state.mn.us/index.php?title=Green_Infrastructure_for_stormwater_management

## Slide 24: What is the recommended soil volume for a tree?
Just make sure it has enough water and nutrients
500 to 1000 cubic feet
1500 to 2500 cubic feet
1 to 3 cubic feet per square foot of canopy

## Slide 25: Technical guidance and specifications

## Slide 26: Tools

## Slide 27: Case studies

## Slide 28: Links

## Slide 29: Outreach and communication

## Slide 30: Touring the MN Stormwater Manual

## Slide 32: Questions? Mike Trojan mike.trojan@state.mn.us Link to Manual – easiest to get there by doing a search on Minnesota Stormwater Manual https://stormwater.pca.state.mn.us/index.php?title=Main_Page