## Slide 1: Minnesota’s Stormwater Manual – Connecting Stormwater Management to the Landscape
Mike Trojan
Minnesota Pollution Control Agency
Northern Green Expo
January 3, 2018

## Slide 2: Topics covered
A little bit on stormwater
Stormwater management timeline
Green Infrastructure and sustainable stormwater management
Overview of the Minnesota Stormwater Manual
How the manual is evolving to incorporate sustainable stormwater management
Quizzes

## Slide 3: A little bit on stormwater
Stormwater runoff is the portion of stormwater that runs off to surface water (lake, river, wetland)
This presentation focuses on urban stormwater runoff, but many of the principles can be applied to agriculture or other settings

## Slide 4: The problem with stormwater runoff
Chart: 
| Agriculture | Hydromodification | Natural causes | Urban runoff | Silviculture | Construction
Percent contribution to waters that are impaired | 29.5 | 6.9 | 3.9 | 3.8 | 2.4 | 1.5
Pollutants in stormwater include sediment, phosphorus, nitrogen, bacteria, organics, metals, and others
The numbers for urban look small, but on a load per area basis they are large
Source: EPA (2005)

## Slide 5: Phosphorus concentrations greater than 40 to 60 ppb typically are problematic for lakes. Typical phosphorus concentrations in urban stormwater runoff are
Less than this concentration
About this concentration
5 times this concentration
10 times this concentration
Quiz 1

## Slide 6
Chart: Concentrations in runoff (ppm)
| TSS | Phosphorus (x 100) | Nitrogen (x 10)
Residential | 27 | 33 | 22.9
Commercial | 87 | 29 | 30
Industrial | 94 | 31 | 17.9
Row crop runoff | 55.3 | 34.4 | 23.2
Forested | 11.1 | 5.3 | 5
Source: Lin (2004)

## Slide 7: So we build stormwater best management practices (BMPs) to reduce pollution from stormwater runoff
Photo courtesy of Barr Engineering

## Slide 8
1990
2000
1980
2010
2020
Pipes and ponds
Low Impact Development
Better Site Design
Image courtesy of the Capitol Region Watershed District
Green Infrastructure/Sustainable stormwater management
A stormwater timeline

## Slide 9: What is sustainable stormwater management?
Managing stormwater in a manner that limits impacts to natural functions of landscapes, hydrologic systems, and habitats (Porter, 2007; Managing Growth in America’s Communities)
  Reuse/replace treated water
  Flood control
  Habitat/biodiversity
  Climate mitigation/adaptation
  Pollutant reduction
  Ecosystem services (e.g. pollination)
  Restore hydrology/recharge groundwater
  Social, economic and other environmental benefits

## Slide 10: Green Infrastructure is the approach used to achieve sustainable stormwater management
Use of stormwater infiltration practices
Harvesting and using stormwater runoff
Disconnecting hard surfaces
Using vegetation
Landscaping
Education
Stormwater Park; Mississippi Watershed Management Organization

## Slide 11: Which of these stormwater practices is generally not considered to be a green infrastructure practice?
Sand filter
Green roof
Constructed wetland
Permeable pavement
Quiz 2

## Slide 12: Green Infrastructure stormwater - Best Management Practices (BMPs)
Bioretention
Vegetated swale
Tree trench
Infiltration basin
Green roof
Permeable pavement
Harvest and reuse
Disconnection

## Slide 13: What is the Minnesota Stormwater Manual?
A resource that provides guidance and tools to help better manage stormwater

## Slide 14: Who uses the manual?
Chart: 
| Manager | Engineer | Water specialist | Other technical | Other non-technical | Public works | Planner
% of respondents | 26.8 | 19.1 | 11.7 | 10.5 | 9.3 | 7.8 | 4.7
What’s missing?
About
11 million hits to date

## Slide 15: What the manual is not
Not a Green Infrastructure (GI) manual
Not the definitive source of information on GI
A cookbook that you can use at every site

## Slide 16: What the manual is
Still a definitive source for how to build stormwater practices properly
A source of information on a variety of topics for stormwater practitioners
A warehouse of links, references, videos, tools, case studies
Image courtesy of Zurich U.S.

## Slide 17: Let’s take a look inside the manual

## Slide 18: How do I navigate the manual?
Table of contents organized around broad topics
Toolbar
Search box
Links
Page contents

## Slide 19
Think of the manual as 1500+ webpages that are linked

## Slide 29: What is in the Manual?
Guidance on BMP selection
Guidance on BMP implementation
Calculation of pollutant loading
Access to tools
Links and case studies
Guidance complying with regulatory requirements

## Slide 31: A look at the manual

## Slide 38: True or False: Bioretention (rain gardens) is an excellent BMP for climate resiliency
False: Moore and Hunt (2013), in evaluating the effect of several BMP types on climate resiliency, state "Despite accounting for sequestration by vegetation in these systems, only stormwater wetlands and grassed swales were predicted to store more carbon than what was released through construction and maintenance".

## Slide 42: Which of these bioretention (rain garden) design considerations improve habitat?
Utilize native, perennial vegetation
Incorporate trees and shrubs if possible
Maximize length to area ratio of BMP
Evaluate compatibility with nearby habitats
Promote soil/media development, including formation of a leaf/plant litter

## Slide 45: What is the recommended soil volume for a tree?
Just make sure it has enough water and nutrients
500 to 1000 cubic feet
1500 to 2500 cubic feet
1 to 3 cubic feet per square foot of canopy

## Slide 47: Tools

## Slide 48: Case studies

## Slide 49: Outreach and communication

## Slide 50: Things to add
Turf
Media mixes
Permeable pavement
Harvest reuse
Golf courses
MS4 permit encourages GI
Organizations (Master Water Stewards, Blue Thumb, Metro Blooms, Watershed organizations)
Legacy funding (funding page in manual)
Show examples
Plant list

## Slide 51: Questions? Mike Trojan mike.trojan@state.mn.us Link to Manual – easiest to get there by doing a search on Minnesota Stormwater Manual https://stormwater.pca.state.mn.us/index.php?title=Main_Page