## Slide 1: Stormwater infiltration and chloride in groundwater
Mike Trojan
MPCA Stormwater
February 7, 2019

## Slide 2: Outline
Stormwater infiltration - overview
Chloride in urban stormwater runoff
Chloride in our waters
Stormwater infiltration
Fate of chloride in infiltration practices
Estimating chloride loads from infiltration practices
Potential recommendations

## Slide 3: Stormwater infiltration- intentional infiltration of stormwater runoff

## Slide 4: Infiltration BMPs
Bioinfiltration (rain gardens)
Tree trenches/boxes
Infiltration basins/trenches
Pemeable pavement
Some swales

## Slide 5: Infiltration is a preferred method for managing stormwater runoff
  Benefit surface waters
  Mimic natural hydrology
  Use space efficiently
  Provides ecosystem services
  Effectively treat pollutants – except chloride

## Slide 6: Infiltration practices focus recharge
Example: 1 acre of impervious runoff directed to an infiltration basin
Infiltration
basin
Typical design infiltrates 35-75 feet of water annually

## Slide 7: September 10, 2015: Effects of stormwater infiltration on groundwater

## Slide 8: Chloride
Mobile and will move through BMPs
Concentrations in stormwater runoff are highly variable and exceed SMCL during winter and early spring runoff events
Findings
  No retention: Concentrations in effluent and rate of exceedance of standard are function of runoff concentration
  Observed concentrations in shallow groundwater in urban areas are similar to concentrations in runoff
Risk to groundwater:
  High based on mobility
  Some preliminary data suggests a seasonal lag in peak concentration in groundwater
  Concentrations in groundwater not likely to reach 250, but there may be impacts to lakes and streams
From 9/10/15 presentation

## Slide 9: Quality impacts - conclusions
Health risks may exist for certain combinations of land use, treatment practice, pollutant, and receptor
Current guidance and regulations (permits) should provide adequate protection for human health
More research is needed on pathogen occurrence in stormwater runoff and fate in infiltration systems, particularly non-vegetated systems
Chloride cannot be treated with stormwater BMPs
  Prevention is the only effective management tool
  Need to better understand dynamics of chloride in urban systems

## Slide 10
MN Groundwater Association white paper: Impacts of stormwater infiltration on chloride in groundwater
The group is still working on the white paper

## Slide 11: Potential fate of infiltrated water

## Slide 20
A little bit about chloride
Does not easily precipitate
Is not biodegradable
Is not readily involved in biological processes
Does not adsorb significantly to mineral/soil surfaces
It is therefore assumed to readily move with water

## Slide 21: Primary anthropogenic sources are road salt, fertilizers, and WWTPs
Cl contributions, Minnesota (From Overbo et al., 2019)
Total = 968,300 tons annually

## Slide 22
Chloride water quality standards
Aquatic life (EPA, 1985)
  Chronic toxicity = 230 mg/L (4 day average, not to be exceeded more than 1 in 3 years)
  Acute toxicity = 860 mg/L (1-hour average not to be exceeded more than 1 in 3 years)
Human consumption – drinking water, secondary maximum contaminant level = 250 mg/L based on salty taste

## Slide 23: Other environmental concerns of chloride
Toxicity in plants (350 mg/L for sensitive species to over 2000 mg/L for tolerant species)
Foliar damage to plants – species dependent; many species show effects above about 200 mg/L
Increased metal mobility – some evidence for Cl complexes with Zn and Cd ; other metals due to ion exchange with the cation
Corrodes steel
Reduced denitrification rates in soil

## Slide 24: Salt application has increased

## Slide 25
Chloride in stormwater runoff
Chart: Chloride (mg/L)
| 43115 | 43146 | 43174 | 43205 | 43235 | 43266 | 43296 | 43327 | 43358 | 43388 | 43419 | 43449
Median | 846.7694 | 338.7078 | 620.9642 | 225.8052 | 70.5641 | 28.2256 | 28.2256 | 28.2256 | 28.2256 | 28.2256 | 21.1692 | 21.1692
Maximum | 9314.4632 | 19757.9521 | 2822.5646 | 846.7694 | 141.1282 | 84.6769 | 56.4513 | 56.4513 | 42.3385 | 56.4513 | 28.2256 | 28.2256
Granato and Smith, 1999
Chart: Chloride (mg/L)
| 43586 | 43692 | 43770
High application rate | 370 | 92 | 78
Low application rate | 45.8 | 39.5 | 11
Winston et al. (2016)
In a MN location with high deicer application rates, 97% of the Cl load was associated with 16% of the total annual runoff volume (Herb, 2018)

## Slide 26
Chloride in surface water (MPCA, 2018)

## Slide 27
Chloride in groundwater (MPCA, 2013)
Shallow sand & gravel aquifers
Bedrock aquifers

## Slide 28: Summary of water quality status
Statewide
  26 lakes were impaired as of 2018
  24 streams impaired as of 2018
  120 lakes classified as at risk (> 1 sample in past 10 years with Cl > 207 mg/L)
Twin Cities Metro
  23 lakes impaired
  17 streams impaired
  38 lakes classified as at risk
  340 assessed waterbodies (11% impaired; 11% insufficient data)
  30% of shallow wells exceed the SMCL
Source: Draft Statewide Chloride Management Plan

## Slide 29
Lakes - % increase per year
Lake trends
(Source: Draft Chloride Management Plan)
Upward trends in 46 of 69 lakes in TCMA
Outside TCMA, upward trends in 14 of 45 lakes
Rate of increase is greatest in lakes in TCMA urban core

## Slide 30
Flow-Adjusted Cl Trends, 1985–2015
(Met Council, 2018)
Upward trends at all but one location
Concentrations well below aquatic life standard

## Slide 31
Groundwater trends
(Source: MPCA 2013)
Upward trends in 11 of 36 wells in shallow sand/gravel aquifers
Average rate of increase was 3.4 mg/L/yr, but rates were much higher is some wells

## Slide 32: Villanova study, Machusick, 2009
MW2
MW3
35 feet
Lysimeters
Rain garden
20 feet
Groundwater flow

## Slide 33
Chart: 
| 39401 | 39425 | 39464 | 39538 | 39541 | 39549 | 39595
Runoff | 3.84 | 2799 | 8521 | 35.5 | 6.38 | 44
Chart: 
| 39401 | 39425 | 39464 | 39538 | 39541 | 39549 | 39595
Runoff | 3.84 | 2799 | 8521 | 35.5 | 6.38 | 44
Lys - 0 | 6.05 | 7.85 | 394 | 65.2 | 47.4 | 9.2
Lys - 4 | 2.89 | 1.42 | 398 | 376 | 382 | 319 | 159
Lys - 8 | 1.53 | 440 | 310 | 365 | 325 | 24.5
Chart: 
| 39401 | 39425 | 39464 | 39538 | 39541 | 39549 | 39595
Runoff | 3.84 | 2799 | 8521 | 35.5 | 6.38 | 44
Lys - 0 | 6.05 | 7.85 | 394 | 65.2 | 47.4 | 9.2
Lys - 4 | 2.89 | 1.42 | 398 | 376 | 382 | 319 | 159
Lys - 8 | 1.53 | 440 | 310 | 365 | 325 | 24.5
MW2 | 24.4 | 3.38 | 53.3 | 290 | 294 | 276 | 104
MW3 | 120.4 | 94.5 | 83.1 | 80.7 | 61.5 | 69.5 | 90.8
Deicers applied
Chart: 
| 39401 | 39425 | 39464 | 39538 | 39541 | 39549 | 39595
Runoff | 3.84 | 2799 | 8521 | 35.5 | 6.38 | 44
Lys - 0 | 6.05 | 7.85 | 394 | 65.2 | 47.4 | 9.2
Lys - 4 | 2.89 | 1.42 | 398 | 376 | 382 | 319 | 159
Lys - 8 | 1.53 | 440 | 310 | 365 | 325 | 24.5
MW2 | 24.4 | 3.38 | 53.3 | 290 | 294 | 276 | 104
Runoff
Lysimeters (0, 4, 8 ft)
MW2
MW3

## Slide 34: Estimating chloride loads from infiltration practices
Clgw = Iperv + Iimperv + Lpi + Lww + Lsw + SW + Iponds + Ifilt + Iinfil
Groundwater
Iperv
Iimperv
Iinfil
Ifilt
Iponds
SW
Lsw
Lww
Lpi

## Slide 35: These next slides are DRAFT

## Slide 36
Chart: 
| Direct infiltration | Impervious surfaces | Piped inflow | Sanitary sewer leakage | Storm sewer leakage | Stormwater infiltration | Surface water discharges | Constructed ponds | Non-infiltration SCMs
% of loading | 40 | 8.6 | 7.1 | 10.8 | 3.6 | 13.3 | 0 | 14.7 | 2

## Slide 37
Chart: 
Chart: 
| Direct infiltration | Impervious surfaces | Piped inflow | Sanitary sewer leakage | Storm sewer leakage | Stormwater infiltration | Surface water discharges | Constructed ponds | Non-infiltration SCMs
% of loading | 2 | 15.4 | 0.8 | 1.2 | 7.9 | 67.9 | 0 | 1.9 | 0
(934 lbs/ac/yr)

## Slide 39
Chart: Top concentration (mg/L)
| 155 | 137 | 95 | 301 | 158 | 202 | 178.5 | 119.5 | 120 | 115 | 177 | 183 | 168 | 198 | 189
bottom | 209 | 232 | 259 | 268 | 184 | 218 | 182.5 | 72 | 120 | 187 | 288 | 284.5 | 403.5 | 575 | 509
Bottom concentrations increase relative to top concentrations
1:1 line

## Slide 40: What are the consequences of high chloride concentrations in lakes?
Community structure (Hintz et al., 2017)
  Negative impact of salinity on zooplankton
  Positive response by phytoplankton
  Mixed results for benthic communities
    Periphyton and snail grazers unaffected
    Biomass of filamentous algae decreased due to competition with phytoplankton
    Direct negative impacts to filamentous algae, amphipods, and some snails and clams
Chemostratification (Novotny and Stefan, 2012)
  Disrupts nutrient cycling
  Prevents oxygen from reaching lake bottom
  Implications for phosphorus export

## Slide 41
Chloride concentrations are a function of baseflow
Miller Creek, Duluth
Bassett Creek, Minneapolis
Source: Bassett Creek WMC

## Slide 42: What are the consequences of high chloride concentrations in streams?
Tiwari and Rachlin (2018)
  Began seeing minor negative impacts above 150 mg/L
  Streambank vegetation changed, but not nutrient cycling
Blasius and Merritt (2002) – most sensitive insects impacted at about 240 mg/L but many unaffected at acute standard
Maryland DNR (2014)
  Benthic IBI declined at 190 mg/L
  All BIBI indicate impairment at 500 mg/L
  Greatest fish effects are on early life stages
Despite considerable information in the literature, difficult to make general statements about ecological effects

## Slide 43: Cl in shallow glacial aquifers, northern U.S. (Mullaney et al., 2009)

## Slide 44
Chart: Chloride concentrations by land use
| Commercial/industrial (N=43) | Sewered residential n=50) | Residential SSTS (n=51) | Agricultural n=113) | Undeveloped (n=50)
Median | 81.8 | 44.6 | 16.1 | 14.1 | 1.1
Maximum | 790 | 463 | 429 | 308 | 97
Cl in shallow groundwater – Minnesota (MPCA)

## Slide 45: Factors affecting Cl in shallow glacial aquifers, northern U.S. (Mullaney et al., 2009)
Significant regressions (p < 0.05)
  Major road density
Not significant
  Highway connector density
  Major highway density
  Highway density
  Local road density
  % residential, commercial, industrial, or transportation land use
  Population density
  Season
Chart: Median rank of Cl concentration
| winter | spring | summer | fall
Median rank | 22 | 22 | 27 | 31
p = 0.94
MPCA, 2002

## Slide 46: What are the consequences of high chloride concentrations in groundwater?
Urban streams with significant baseflow are potentially at risk
Shallow sand and gravel aquifers are at risk in core urban areas – is this a concern?
  There are few groundwater receptors
  Is salty taste more important than impacts to aquatic ecosystems?
What about deeper drinking water aquifers?

## Slide 47: Much of the core Metro Area aquifer system has low-moderate vulnerability
We currently have insufficient data to assess trends in deeper aquifers

## Slide 48: Management strategies
Decrease use of chloride deicers
Use alternatives (maybe)
Use liquids (anti-icing)
Establish chloride free zones near receiving waters
Improve snow/ice removal technology
Lower winter speed limits
Infiltrate in the right locations, especially with permeable pavements

## Slide 49: Stormwater infiltration recommendations
Infiltrate in areas not vulnerable to chloride contamination
In vulnerable areas, if infiltration is employed, distribute infiltration practices instead of focusing on a single location
Properly site infiltration practices with respect to receiving waters
Utilize permeable pavement when appropriate

## Slide 50: Needs
Analyze trend data for Metro streams – Met Council starting this
Improve understanding of fate and transport in groundwater
  Map vulnerable areas
  Enhance monitoring in these areas
  Monitor deeper aquifers in vulnerable areas
Improve understanding of impacts in lakes
  Study chloride dynamics in impacted lakes
  Study ecological effects
  Study phosphorus dynamics
Identify high value waters that are at risk
More research on chloride alternatives

## Slide 51: Chloride is attenuated
Delayed peaks in groundwater
Lower max concentrations
Elevated concentrations persist in groundwater

## Slide 52: Summary
Runoff
  Very high concentrations and bulk of mass for a handful of events
  Low concentrations and loading for rest of the year
Cl- is attenuated in infiltration practices
Groundwater
  Infiltration reduces winter peaks
  Cl- enriched groundwater from spring through fall

## Slide 53: Potential recommendations
Infiltrate
  in areas with low-moderate road salt inputs
  where surface streams are vulnerable
Potential concerns in areas that contribute significantly to aquifer recharge
Infiltration practices
  Do not use to store salt-laden snow
  Permeable pavement should be encouraged

## Slide 54: Ultimately, source reduction is the only way to effectively manage chloride
Questions?