## Slide 1
Do we have a chloride problem in our water?
Mike Trojan
MPCA Stormwater
March 8, 2019

## Slide 2: YES
Thank you and are there any questions?

## Slide 3: Disclaimer
I’m not specifically working on chloride. There is on-going research. To the extent time allowed I reviewed literature and talked with people working on the issue to gain perspective on different aspects of this issue. But be aware that I’m not engaged in research around chloride. Hopefully I’ll qualify my statements appropriately and suggest areas where we need more information.

## Slide 4: Outline
A little bit about chloride
Big picture: Chloride concentrations and trends in Minnesota waters
Taking a closer look in urban areas
What are we doing to manage chloride?
Knowledge gaps
Wrap-up

## Slide 6
A little bit about chloride
Does not easily precipitate
Is not biodegradable
Is not readily involved in biological processes
Does not adsorb significantly to mineral/soil surfaces
It is therefore assumed to readily move with water

## Slide 7: Primary anthropogenic sources are road salt, fertilizers, and WWTPs
Fraction of annual chloride contributions from major point and nonpoint sources for State of Minnesota (From Overbo et al., 2019)
Total = 968,300 tons annually

## Slide 8
Chloride in stormwater runoff
Chart: Chloride (mg/L)
| 43115 | 43146 | 43174 | 43205 | 43235 | 43266 | 43296 | 43327 | 43358 | 43388 | 43419 | 43449
Median | 846.7694 | 338.7078 | 620.9642 | 225.8052 | 70.5641 | 28.2256 | 28.2256 | 28.2256 | 28.2256 | 28.2256 | 21.1692 | 21.1692
Maximum | 9314.4632 | 19757.9521 | 2822.5646 | 846.7694 | 141.1282 | 84.6769 | 56.4513 | 56.4513 | 42.3385 | 56.4513 | 28.2256 | 28.2256
Runoff (from Granato and Smith, 1999)

## Slide 9
At what concentration is chloride a concern?
Aquatic life (EPA, 1985)
  Chronic toxicity = 230 mg/L (4 day average, not to be exceeded more than 1 in 3 years
  Acute toxicity = 860 mg/L (1-hour average not to be exceeded more than 1 in 3 years)
Human consumption – drinking water, secondary maximum contaminant level = 250 mg/L based on salty taste

## Slide 10: Other environmental concerns
Chloride toxicity in plants (350 mg/L for sensitive species to over 2000 mg/L for tolerant species)
Foliar damage to plants – species dependent; many species show effects above about 200 mg/L
Increased metal mobility – a complex issue, but some evidence for Cl complexes with Zn and Cd ; other metals appears to be due to ion exchange with the cation
Corrodes steel

## Slide 11
Chloride in surface water (MPCA, 2018)

## Slide 12
Cl in groundwater (MPCA, 2013)
Shallow sand & gravel aquifers
Bedrock aquifers

## Slide 13: Summary of water quality status
Statewide
  26 lakes were impaired as of 2018
  24 streams impaired as of 2018
  120 lakes classified as at risk (> 1 sample in past 10 years with Cl > 207 mg/L)
Twin Cities Metro
  23 lakes impaired
  17 streams impaired
  38 lakes classified as at risk
  340 assessed waterbodies (11% impaired; 11% insufficient data)
  30% of shallow wells exceed the SMCL
Source: Draft Statewide Chloride Management Plan

## Slide 14
Lakes - % increase per year
Lake trends
(Source: Draft Chloride Management Plan)
Upward trends in 46 of 69 lakes in TCMA
Outside TCMA, upward trends in 14 of 45 lakes
Rate of increase is greatest in lakes in TCMA urban core

## Slide 15
Flow-Adjusted Cl Trends, 1985–2015
(Met Council, 2018)
Upward trends at all but one location
Concentrations well below aquatic life standard

## Slide 16
Groundwater trends
(Source: MPCA 2013)
Upward trends in 11 of 36 wells in shallow sand/gravel aquifers
Average rate of increase was 3.4 mg/L/yr, but rates were much higher is some wells

## Slide 17: Initial conclusions
Chloride is a concern in surface waters in core urban areas
Concentrations in shallow groundwater in urban core areas is significantly impacted
Outside urban areas, chloride is, in general, not a concern, although there are local exceptions
In suburban and exurban areas, results are mixed

## Slide 18: Taking a closer look - lakes
What factors make a lake vulnerable to chloride contamination?
What are the consequences of high chloride concentrations in lakes?
Should we be concerned/questions we might want to ask?

## Slide 19: Potential factors affecting lake vulnerability
Deicer application rates
Imperviousness
Lake characteristics
  Depth
  Area
  Watershed area

## Slide 20: Road density and imperviousness (Dugan et al., 2017)
Impervious surface and road density within 500 meters of a lake were strong predictors of increasing Cl concentrations in the lake (n=284)
Upward concentration trends observed at impervious values > 1%

## Slide 21: What are the consequences of high chloride concentrations in lakes?
Community structure (Hintz et al., 2017)
  Negative impact of salinity on zooplankton
  Positive response by phytoplankton
  Mixed results for benthic communities
    Periphyton and snail grazers unaffected
    Biomass of filamentous algae decreased due to competition with phytoplankton
    Direct negative impacts to filamentous algae, amphipods, and some snails and clams

## Slide 22
Chart: Bottom concentration (mg/L)
| 209 | 232 | 259 | 268 | 184 | 218 | 182.5 | 72 | 120 | 187 | 288 | 284.5 | 403.5 | 575 | 509
ratio | 1.3484 | 1.6934 | 2.7263 | 0.89037 | 1.1646 | 1.0792 | 1.0224 | 0.60251 | 1 | 1.6261 | 1.6271 | 1.5546 | 2.4018 | 2.904 | 2.6931
Chart: Maximum depth (ft)
| 30 | 25 | 63 | 16 | 46 | 36 | 12 | 9 | 15.5 | 47 | 37 | 28 | 24 | 28 | 47
bottom | 209 | 232 | 259 | 268 | 184 | 218 | 182.5 | 72 | 120 | 187 | 288 | 284.5 | 403.5 | 575 | 509

## Slide 24: Management strategies
Decrease use of chloride deicers
Use alternatives
Use liquids
Establish chloride free zones near receiving waters
Improve snow/ice removal technology
Permeable pavement
Lower winter speed limits
Infiltrate in the right locations
Accept the loss of some waters