## Slide 1
Limitations of Using Stormwater Ponds for Phosphorus Control
Joe Bischoff
Brian Beck
Bill James
January 9, 2017

## Slide 3: Presentation Objectives
Overview of Watershed Phosphorus Cycle
  Sources and management
Constructed Ponds and Stormwater Wetlands as Phosphorus Sinks
  General design
  Sediment phosphorus burial and release
  Implications for watershed phosphorus loading
Understanding and Managing Watershed Sediment Phosphorus Pools
  Modeling approaches for identifying sediment P sources
  Management approaches for sediment P sources

## Slide 4: The Problem
Shingle Creek Watershed Management Commission
Since 2005, $12 million invested in water quality projects
Municipal retrofits, $2.7M
MNDOT and County water quality projects, $2M
Total Phosphorus (mg/L)
Year
Shingle Creek Outlet
Notes: Even with heavy investment in watershed BMPs and source management, often little progress is made in reducing watershed P loading
  So, how do we move forward

## Slide 5
2010-2012
TP= 243 µg/L
SRP = 101 µg/L
TSS = 18 mg/L
2010-2012
TP= 199 µg/L
SRP = 108 µg/L
TSS = 62 mg/L
2015 only
TP = 170 µg/L
SRP = 63 µg/L
TSS = 6.5 mg/L
Bass Lake Watershed Phosphorus Reduction Project (5-year TMDL review monitoring)

## Slide 6: Watershed Phosphorus Management The Traditional Stormwater Paradigm
Phosphorus Source Management
  Phosphorus fertilizer ban
  Homeowner best practices
    Grass clippings, runoff management
  Street sweeping
Provide phosphorus sinks in the watershed
  Constructed ponds to settle particulate phosphorus
  Wetlands to settle and adsorb phosphorus
  Rain gardens and biofilters
Notes: Map of watershed with ponds

## Slide 7: Standard Constructed Pond Design
Source: Minnesota Stormwater Manual
A 4-foot mean depth and volume equal to the runoff volume from a 2.5-inch, 24-hour rainfall event over the watershed, or 1800 cubic feet per acre of drainage to the basin, or 3600 cubic feet per acre of drainage area for enhanced phosphorus removal.
Notes: Where phosphorus load reductions are a priority, it is Recommended that a maximum depth of 8 feet be used, to limit the likelihood of stratification and the potential for bottom sediment to release phosphorus.

## Slide 8: Sediment Phosphorus Cycle
Sondergaard et al. 2001

## Slide 9
What is Causing Sediment Phosphorus Release?
-
16
-
14
-
12
-
10
-
8
-
6
-
4
-
2
0
0
1
2
3
Sediment depth (cm)
Redox
-
-
1
-
Burial of phosphorus
Release of Phosphorus
Sediment Redox Reactions
Anoxic Conditions
Mobile Phosphorus (mg/g)
Notes:   Historic equilibrium phosphorus concentrations represent a balance between burial and release
  Elevated phosphorus in sediment will diffuse into surface waters
    This cycle will continue until the sediment phosphorus peak is reduced

## Slide 10: Anoxia in Stormwater Ponds and Wetlands
Pond Monitoring
6 stormwater ponds and wetlands in Chanhassen and Eden Prairie
Monitored May through August
Anoxia observed as shallow as 3 feet in ponds
Source: Riley Purgatory Bluff Creek Watershed District 2013 Pond Monitoring Report

## Slide 11: Eagan Pond JP-5
Receives discharge from Fish Lake
Discharges to Blackhawk Lake
Pond is undersized
Max depth of 8 feet
Concerned adding phosphorus to discharge and inadequately treating watershed runoff
6
7
5

## Slide 12
5.2 mg/m2/day
0.6 mg/m2/day

## Slide 13: Pond/Stormwater Wetland JP-5 City of Eagan
Mobile P (mg/g)
Mobile P (mg/g)
Mobile P (mg/g)

## Slide 14: Urban Pond Sediment Chemistry City of Eagan

## Slide 15: Pond Inspection Program Eden Prairie, Minnesota
MS4 Permit requires annual inspection of stormwater ponds
  Identify those with maintenance issues
  Identify ponds that are losing dead storage and settling effectiveness
  Identify critical ponds in treatment train
  Over 1,400 stormwater ponds and wetlands
    Mix of private and public ownership
  Systematically working through City
  Almost $1,000,000 in inspection costs

## Slide 16: Mitchell Lake Watershed
Mitchell
Lake
Parameter | Mitchell Lake
Surface Area (acres) | 120
Average Depth (feet) | 5.0
Maximum Depth (feet) | 20
Volume (acre-feet) | 598
Residence Time (years) | 0.7
Littoral Area (acres) | 120
Littoral Area (%) | 100%
Watershed (acres) | 943
Stormwater Ponds | 45

## Slide 17
Mitchell
Lake
18-14-B
18-41-B
18-13-A
Mitchell Lake Subwatershed
Eden Prairie, Minnesota

## Slide 18: Pond Inspection Results
Basin ID | Pond Type | Surveyed Permanent Pool Volume (AF) | NURP Ratio1 | P8 TP Removal (%) | P8 TP Concentration (µg/L) | Monitored TP Concentration (µg/L)
18-41-B | Stormwater Wetland | 1.45 | 4.7 | 33 | 105 | 1,912
18-13-A | Stormwater Wetland | 1.24 | 1.0 | 12 | 153 | 335
18-14-B | Stormwater Wetland | 10.16 | 1.5 | 26 | 134 | 254
07-43-A | Constructed Pond | 2.3 | 1.3 | 55 | 136 | 720
1 The NURP ratio is based on the cumulative area and dead storage to account for basins in sequence. Values over 1 exceed NURP standards and values under 1 do not meet NURP standards.

## Slide 19
Chart: Modeled and Monitored TP Mitchell Lake Watershed
| 07-43-A | 07-44-A | 08-34-A | 17-13-A | 18-13-A | 18-13-B | 18-14-B | 18-41-B
P8 Modeled | 0.1358 | 0.1086 | 0.117 | 0.1088 | 0.1531 | 0.1233 | 0.1336 | 0.1045
Monitored | 0.72 | 0.5575 | 0.3275 | 0.071375 | 0.335 | 0.92 | 0.25429 | 1.912

## Slide 20: Assessment Approaches Modeling Considerations
City of Eagan Ponds | LP-41 | LP-44
Pond Area (acres) | 4.8 | 2.4
Pond P release (lbs/yr) 1 | 9.7 | 4.9
Pond TP Sedimentation (lbs/yr) 2 | 8.6 | 6.5
Sediment Redox P (pounds) | 728 | 33
Sediment Mobile P (pounds) | 1,295 | 227
1 Assumes release of 5 mg/m2/day and 45 days anoxia
2 2008-2012 average using PondNet
    City of Eagan, MN has over 1,200 Stormwater wetlands and constructed ponds over 34.5 square miles

## Slide 21: Management of P Release in Stormwater Ponds
Sediment Excavation and Disposal
Increase dead storage to improve settling
Remove high phosphorus sediments
Sediment Phosphorus Inactivation
Aluminum, iron, lanthanum
Dissolved Oxygen Management
  Eliminate anoxic release of sediment P
Notes: Implications for watershed phosphorus loading

## Slide 22: Sediment Removal and Disposal
Excavation for improved settling efficiency
  Increase dead storage to improve settling to remove additional particulate P
  Excavation and disposal are typically expensive
    Contaminated sediments must be landfilled
  Limited by wetland regulations in stormwater wetlands
Basin ID | Estimated Excavation Costs | Priority | TP Reduction | Cost per pound P removal
 |  |  | (lb/yr) | $
14-43-A | $69,000 | Medium | 0.3 | $7,667
14-34-A | $81,000 | High | 1.4 | $1,929
24-33-A | $110,000 | High | 0.9 | $4,074
24-33-C | $195,000 | Medium | 0.8 | $8,125

## Slide 23: BMP Cost Efficiency

## Slide 24: Excavation for Phosphorus Control
Mobile P (mg/g)

## Slide 25: Sediment Phosphorus Inactivation
Aluminum Sulfate (liquid)
  Dissolves in water to form aluminum hydroxide and sulfate
  Aluminum hydroxide is a white solid that settles out of the water column
Permanently binds phosphorus in the sediments
Aluminum phosphate complexation (Al(OH)3PO4)
  Very stable in the environment
  Not sensitive to anoxia (low oxygen)
Alum has been used in hundreds of lakes throughout the world to reduce P cycling

## Slide 26: Assessment Approaches Modeling Considerations
City of Eagan Ponds | LP-41 | LP-44
Pond Area (acres) | 4.8 | 2.4
Pond P release (lbs/yr) 1 | 9.7 | 4.9
Pond TP Sedimentation (lbs/yr) 2 | 8.6 | 6.5
Sediment Redox P (pounds) | 728 | 33
Sediment Mobile P (pounds) | 1,295 | 227
Alum Inactivation Cost3 | $137,000 | $39,000
Alum Treatment Frequency4 (years) | 6 | 16
Cost ($ per treatment) | $10,000 | 
Cost ($ per 30 year life cycle) | $187,000 | $59,000
1 Assumes release of 5 mg/m2/day and 45 days anoxia
2 2008-2012 average using PondNet
3Based on inactivating 90% of mobile P in top 5 cm
4 Assumes 43% and 23% of settled TP is mobile P respectively and minimum dose of 50 g Al/m 2

## Slide 27: Chanhassen Pond LLP 10.4
Residents complained of foul odors
  Could be result of dead algae (filamentous), decaying plant material, or hydrogen sulfide production
  No water quality data available
  Clear hydrogen sulfide production from anoxic sediments
  Heavy duckweed coverage
Solution
Sediment P inactivation
Aeration to control hydrogen sulfide production

## Slide 28: Summary
Stormwater ponds and wetlands are potential sources of phosphorus
  Offsetting watershed phosphorus BMPs
  Transformers of P: settling particulate P, releasing dissolved P
  Release is driven by anoxia and sediment mobile phosphorus
Quantifying watershed wide sediment phosphorus pools and dissolved oxygen dynamics is critical
  Good sediment and DO data is invaluable
  Mobile phosphorus in pond and wetland sediments
  Anoxia as the driver of P release
Standard maintenance techniques are not cost effective or feasible in most cases
Sediment removal is expensive, limited by wetland regulations and does not address P release

## Slide 29: Questions? Joe Bischoff jbischoff@Wenck.com