## Slide 1: MIDS Calculator Fundamentals

## Slide 2: MIDS Calculator Fundamentals

## Slide 3: Presentation outline
Review MIDS performance goals
Volume reduction conformance calculations
Pollutant removal calculations
Pollutant load reduction calculations
Other calculator notes and functions
Notes: Calculator can be used for other goals as well. For example, a more strict local goal or a less strict goal for projects not requiring a permit. Or perhaps a TMDL application. Doesn’t need to be restricted to the “1.1” goal.

## Slide 4: MIDS calculator
Primary function of calculator is to evaluate site conformance to MIDS performance goals
MIDS performance goals vary depending on site characteristics
MIDS “Flexible Treatment Options” include
  Volume retention requirements
  % annual phosphorus removal requirements
Notes: Calculator can be used for other goals as well. For example, a more strict local goal or a less strict goal for projects not requiring a permit. Or perhaps a TMDL application. Doesn’t need to be restricted to the “1.1” goal.

## Slide 5: A simplification of Flexible Treatment Options…
“Primary” Performance Goal:
Retain 1.1 inch x Impervious Surface Area
Good Infiltration
YES
No Infiltration
Restrictions (clay, contaminants, etc.) but space for BMP
Slow Infiltration
Limited space, but some available
Retain 0.55 inch x Impervious Surface Area
AND
75% Annual TP Removal
YES
Volume retention to maximum extent possible
AND
60% Annual TP Removal
YES
NO
NO
NO
Offsite Mitigation
Notes: Calculator can be used for other goals as well. For example, a more strict local goal or a less strict goal for projects not requiring a permit. Or perhaps a TMDL application. Doesn’t need to be restricted to the “1.1” goal.

## Slide 6: MIDS calculator
Evaluates site conformance to MIDS performance goals, including
  Volume reduction
  % Annual Pollutant Removals (TP, DP, TSS)
  No rate control
Can be used to evaluate conformance to other goals (more/less stringent rules, TMDLs, etc.)
    Estimates annual runoff volume and pollutant load reductions
Notes: Calculator can be used for other goals as well. For example, a more strict local goal or a less strict goal for projects not requiring a permit. Or perhaps a TMDL application. Doesn’t need to be restricted to the “1.1” goal.

## Slide 7: MIDS Calculator
    Calculator ensures crediting method(s) consistent with underlying assumptions of performance goal development modeling

## Slide 8: Jargon
Performance goal: Stormwater standard/rule
Credit: Quantity of stormwater volume or pollutant reduction achieved by an individual BMP or cumulatively with multiple BMPs
Volume retention/reduction = volume infiltrated or evaporated instead of leaving site as runoff
TP: Total Phosphorus
DP: Dissolved Phosphorus
TSS: Total Suspended Sediment
Notes: SW Manual definition of Credit:
There is no universal definition for the term stormwater credit. As used in this manual, credit refers to the quantity of stormwater or pollutant reduction achieved either by an individual BMP or cumulatively with multiple BMPs. Examples include the following.
A rain garden infiltrates 50,000 cubic feet of water per year. The rain garden receives a credit of 50,000 cubic feet to be applied toward runoff reduction (volume control).
A rain garden results in the removal of 10 pounds of phosphorus per year from stormwater runoff. The rain garden receives a credit of 10 pounds to be applied toward pollutant load reduction.
Three rain gardens each remove 10 pounds of phosphorus per year. Each rain garden receives a credit of 10 pounds, resulting in a total credit of 30 pounds.

## Slide 9: Calculating volume reduction conformance
For sites conducive to infiltration,
MIDS volume reduction performance goal:
Volume reduction goal can vary depending on site constraints
=
Required
Retention Volume
X
1.1 inch
Notes: Note from MPCA: This is for most of the BMPs in the calculator but make some mention of the non volume BMPs like swales and how a different approach was needed

## Slide 10: Development of performance goal
Continuous modeling analysis completed to establish 1.1-inch performance goal
  - Simulated 35-years using 15-minute precipitation data
Modeling used to compare average annual runoff volumes from “native” conditions to runoff from developed conditions with infiltration BMPs of varying size
Notes: Performance goal may seem simple, but there is detailed hydrologic and hydraulic analysis behind it (35-year continuous simulation using 15-minute precipitation data)

## Slide 11: Development of performance goal
  Goal not time dependent (instantaneous versus continuous or event-based)
  “Kerplunk” method (Andy Reese terminology)
Notes: Goal is not time dependent. Have to be ready for rain to happen instantaneously. Assume all stormwater runs off at once.

## Slide 12
Calculates required volume retention
Performance goal
(1.1 inches * Impervious Area)
Notes: Required volume retention calculated in cubic feet. So, for most BMPs, this represents the volume of water that needs to be captured by BMP.

## Slide 13
Calculates required volume retention
For 10-acre site with 50% impervious,
required volume retention = 19,965 ft3
Notes: Required volume retention calculated in cubic feet. So, for most BMPs, this represents the volume of water that needs to be captured by BMP.

## Slide 14
Calculates volume reduction achieved to meet MIDS performance goal
(based on entry of site BMP characteristics)
Calculates Volume Retention Achieved
Notes: Details on the calculation of volume reduction in later slides

## Slide 15: Variety of BMPs included in calculator

## Slide 16: Calculating volume reduction conformance
Volume reduction conformance calculated differently for infiltration and filtration
Permeable soil
Volume Captured in Basin =
Volume Infiltrated
Infiltration:
Impermeable soil
Volume Captured in Basin ≠
Volume Infiltrated
Filtration:

## Slide 17: Let’s start with infiltration…
For most infiltration-based BMPs (w/o under drains), MIDS volume reduction achievement based on “instantaneous” retention volume
Permeable soil
Retention Volume

## Slide 18: Calculating volume reduction
Retention Volume
For 10-acre site with 50% impervious,
Required volume retention = 19,965 ft3
Required drawdown = 48 hours
Notes: For 10-acre site with 50% impervious,
Required volume retention = 19,965 ft3

## Slide 19: Calculating volume reduction
Retention Volume
For 10-acre site with 50% impervious,
Required volume retention = 19,965 ft3

## Slide 20: Let’s move on to filtration…
Under Drain at Bottom
Impermeable soil
Impermeable soil
Elevated Under Drain
Two common filtration scenarios:

## Slide 21: Filtration BMPs with under drain at bottom
Significant volume discharged offsite through under drain
Impermeable soil

## Slide 22: But there’s some volume loss, even with a under drain, right?
Infiltration
Volume Losses will occur via:
Infiltration (side slopes and bottom)
Evapotranspiration
Infiltration
Evapotranspiration

## Slide 23: Filtration BMPs with under drain at bottom
For filtration BMPs with under drain at the bottom, MIDS volume reduction is calculated based on:
  Infiltration from bottom and side slopes during required drawdown time (48 or 24 hours)
  Evapotranspiration in 72 hours
Underlying design assumption- under drain should be designed to empty filtration basin in 24 - 48 hours (volume credits will be overestimated if basin drains too fast)
Notes: User indicates whether 24- or 48-hour drawdown time is applicable

## Slide 24: Example: Filtration BMP with under drain at bottom
Impermeable soil
How does volume reduction conformance change with under drain at bottom?
Bioretention basin in B soils (no under drain needed)
Infiltration = 2499 ft3
Evapotranspiration = 297 ft3
Site:
10 acres, 50% Impervious
C soils (infiltration 0.20 in/hr)
Live storage = 1.5 feet
Filtration media depth = 3.8 ft
Area at overflow = 14,641 ft2
Media surface area = 11,881 ft2
Bottom surface area = 7,225 ft2
No tree; Mix C
Field capacity = 0.11
Porosity = 0.25
2,624 ft3
Notes: Site:
10 acres
D soils (assume underlying soils have infiltration rate of 0.06 in/hr)
50% impervious
Performance Goal:
  inches * 10 acres * 50% impervious = 19,965 ft3
BMP: Filtration basin (drain tile at the bottom)
Live storage: 1.5 feet deep
4H:1V side slopes
Media depth: 3 feet
Square basin with top (at overflow) of 121 feet x 121 feet
Vegetation line 1.5 feet below overflow (109 feet x 109 feet)
Bottom of basin 3 feet below vegetation line (85 feet by 85 feet)

## Slide 25: Example: Filtration BMP with under drain at bottom
Total volume retention “credit” with under drain at bottom =
= 2,499 ft3 + 297 ft3
= 2,795 ft3
Compared with volume retention “credit” without under drain = 19,965 ft3
Impermeable soil
How does volume reduction conformance change with under drain at bottom?
Bioretention basin in B soils (no under drain needed)
Infiltration = 2,624 ft3
Evapotranspiration = 460 ft3
2,624 ft3
Notes: 3084/19965= 15% performance goal

## Slide 26: Example: Filtration BMPs with elevated under drain
With elevated under drain, credit is given for volume stored below under drain plus ET and side infiltration
Impermeable soil
Infiltration = 2,624 ft3
Evapotranspiration (ET)

## Slide 27: Filtration BMPs with elevated under drain
Infiltration = 2,624 ft3
Impermeable soil
Evapotranspiration = 297 ft3
Site:
10 acres, 50% Impervious
C soils (infiltration 0.2 in/hr)
Overflow depth = 1.5 feet
Media depth = 3.8 ft
Under drain 0.8 ft from bottom
Area at overflow = 14,641 ft2
Media surface area = 11,881 ft2
Area at under drain = 7,225 ft2
Bottom surface area = 6,178 ft2
No tree; Mix C
Field capacity = 0.11
Porosity = 0.25
Side Slope Infiltration = 890 ft3
Volume stored below under drain = 1,340 ft3
Bottom Infiltration = 1,734 ft3
Notes: I need to check numbers with Eric

## Slide 28: Filtration BMPs with elevated under drain
Total volume retention “credit” with elevated under drain =
1734 ft3 + 890 ft3 + 1340 ft3 + 297 ft3
= 4,261 ft3
Compared with volume retention “credits”:
w/under drain at bottom = 3,084 ft3
without under drain = 19,965 ft3
Impermeable soil
Evapotranspiration = 460 ft3
Side Slope Infiltration = 890 ft3
Volume below under drain = 2,144 ft3

## Slide 29
Questions on volume reduction conformance calculations?

## Slide 30: Fundamentals of MIDS Calculator Pollutant Removal Calculations

## Slide 31: A simplification of Flexible Treatment Options…
“Primary” Performance Goal:
Retain 1.1 inch x Impervious Surface Area
Good Infiltration
YES
No Infiltration
Restrictions (clay, contaminants, etc.) but space for BMP
Slow Infiltration
Limited space, but some available
Retain 0.55 inch x Impervious Surface Area
AND
75% Annual TP Removal
YES
Volume retention to maximum extent possible
AND
60% Annual TP Removal
YES
NO
NO
NO
Offsite Mitigation
Notes: Volume Reduction conformance addresses primary MIDS goal (1.1” from impervious surfaces) and a portion of FTO #2. Other FTOs require calculation of pollutant removals.

## Slide 32: Calculating annual pollutant removal
Calculator estimates % annual pollutant removal achieved
    For each individual BMP
    Cumulative % annual removal for site
    Total Phosphorus (TP), Dissolved Phosphorus (DP), and Total Suspended Sediment (TSS)

## Slide 33: Calculating annual pollutant removal
  Why?
      To show conformance with MIDS Flexible Treatment Options (FTOs) or other local requirements
    - Reduction of TSS & P for TMDLs (Total Maximum Daily Loads)
- Information for grant applications

## Slide 34: Basis of % annual pollutant removal calculations
For volume retained on site, assume 100% pollutant removal
For Volume NOT retained by BMP, assume 0% - 100% pollutant removal
  Depending on BMP
  Depending on if BMP is designed as a flow-through or bypass system
Notes: Mike T didn’t understand the word ”retained”. Maybe say “retained on site”

## Slide 35: Calculating % annual pollutant removal
(100- %RVR) %PR
Total
% Pollutant
Removal
%RVR
Where,
%RVR =
%PR =
% Annual Runoff Volume Retained Onsite
% Pollutant Removal

## Slide 36: Annual pollutant load reduction
100% TSS, PP, DP Reduction
0% TSS, Particulate P (PP), and Dissolved P (DP) Reduction
91% Annual Volume Retained
9 % Annual Volume

## Slide 37: Example calculating % annual pollutant removal from bioretention w/o under drain
(100- %RVR) %PR
Total
% TP
Removal
%RVR
(100- 91) 0%
91%
91%

## Slide 38: Calculating % Pollutant Removal
Many BMPs achieve primary pollutant removal through other mechanisms
  - Filtration
  - Settling
  Adsorption
  Calculator applies % removal assumptions to portions of stormwater not infiltrated

## Slide 39: Runoff and pollutant removal assumptions in calculator
Calculated from performance curves

## Slide 40: Example calculating % annual pollutant removal from filtration basin w/under drain
(100- %RVR) %PR
Annual
% TP
Removal
%RVR
(100- 20) 0.25
20
40%
If a filtration basin infiltrates 20% annual runoff volume,

## Slide 41: Calculating % annual volume retained
So, for a BMP designed to capture 1.1 inches of runoff from impervious surfaces, how does this translate to annual volume removal?
  How does it vary by site imperviousness?
  How does it vary by soil type?
  How does it vary if your BMP is sized for less than 1.1 inches?

## Slide 42: Making the connection: Performance goal to % annual pollutant removal
Required
Retention Volume
(cubic feet)
% Annual Removal

## Slide 43: Making the Connection: “Performance Curves” used to Estimate % Annual Volume Retained
Chart: BMP Volume (cubic feet)
| 0 | 500 | 1000 | 1500 | 1997 | 3993 | 5990 | 7986 | 9983 | 11979 | 13976 | 15972 | 17969 | 19965 | 21962 | 23958 | 25955 | 27951 | 29948 | 31944 | 35937 | 43560 | 50000 | 65000
10% Imp | 0 | 0.25458 | 0.3981 | 0.49542 | 0.56609 | 0.72772 | 0.80522 | 0.85299 | 0.88935 | 0.91703 | 0.93671 | 0.95175 | 0.96214 | 0.96863 | 0.9728 | 0.97663 | 0.98039 | 0.98339 | 0.98578 | 0.98783 | 0.99098 | 0.99501 | 0.99617 | 0.99891
30% Imp | 0 | 0.13066 | 0.2291 | 0.31223 | 0.38389 | 0.58814 | 0.71286 | 0.79596 | 0.85337 | 0.89244 | 0.91934 | 0.93997 | 0.95467 | 0.96479 | 0.97159 | 0.97664 | 0.9807 | 0.98403 | 0.98637 | 0.98842 | 0.99157 | 0.99454 | 0.99558 | 0.99685
= 0.55 inch
Chart: BMP Volume [feet3]
| 0 | 499.99999999999994 | 999.99999999999989 | 1500 | 1997 | 3993.0000000000005 | 5990 | 7986.0000000000009 | 9983 | 11979.000000000002 | 13976 | 15972.000000000002 | 17969 | 19965 | 21962 | 23958.000000000004 | 25955 | 27951.000000000007 | 29948 | 31944.000000000004 | 35937 | 43560 | 49999.999999999993 | 65000 | 87120
A soils | 0 | 0.14507 | 0.24757 | 0.33191 | 0.40209 | 0.60469 | 0.72712 | 0.80583 | 0.86042 | 0.89834 | 0.92449 | 0.943 | 0.95652 | 0.96648 | 0.97359 | 0.97955 | 0.98381 | 0.98666 | 0.98886 | 0.99045 | 0.99316 | 0.99631 | 0.99705 | 0.99817 | 1
B Soils | 0 | 0.08622 | 0.15615 | 0.21821 | 0.27432 | 0.45674 | 0.58479 | 0.67795 | 0.74834 | 0.80268 | 0.84518 | 0.87872 | 0.90375 | 0.92284 | 0.93727 | 0.94861 | 0.958 | 0.96566 | 0.97167 | 0.97607 | 0.98274 | 0.9902 | 0.99355 | 0.99626 | 1
C Soils | 0 | 0.061383 | 0.1167 | 0.16761 | 0.21467 | 0.37512 | 0.49733 | 0.59148 | 0.66454 | 0.72393 | 0.77226 | 0.8115 | 0.84342 | 0.86943 | 0.8904 | 0.90739 | 0.92181 | 0.93405 | 0.94454 | 0.95327 | 0.96566 | 0.97946 | 0.98627 | 0.99411 | 1
= 0.55 inch
= 1.1 inch

## Slide 44: Calculating % annual volume retained
Performance curves were developed to determine annual volume reduction (%RVR) for most volume-reduction BMPs in calculator
  This approach allows flexibility for designers (not one size fits all)
  Utilize modeling results to develop performance curves
  Example BMPs: Bioretention, permeable pavement, infiltration trenches

## Slide 45
Questions on pollutant removal calculations?

## Slide 46: Calculating Pollutant Load Reductions in MIDS Calculator

## Slide 47: Pollutant loading basics
year
H2O
P
Pollutant
Load
[mass/time]
Runoff
Volume
[volume/time]
Pollutant
Concentration
[mass/volume]
=
x
Notes: Often use the term ‘pollutant loading’
Pollutant Loading is a measurement of the amount (or mass) of pollutant generated over a given period of time.

## Slide 48: Estimating pollutant load reductions in MIDS calculator
Estimate pollutant load from site using Simple Method
  - e.g., How much phosphorus is being generated from your developed site before BMPs?
2. Apply % Pollutant Removal to estimate annual pollutant load reduction
  - e.g., What phosphorus load reduction can be expected if your BMP removes 50% annual TP?
Notes: This was confusing for us. Maybe just make the last point a #3. It feels like the third step in the process

## Slide 49: Calculating annual pollutant load: the Simple Method
Equation developed by Tom Schueler in 1987
Estimates runoff volume and pollutant loads on an annual basis
Requires easily obtainable data

## Slide 50
Simplified runoff volume calculation based on the following inputs:
- Drainage Area
- Annual rainfall
- % Impervious, turf, and forest to calculate runoff coefficient
Pollutant concentration for TP and TSS based on literature values for stormwater
Calculating annual pollutant load: the Simple Method

## Slide 51: Estimating pollutant load reductions in MIDS calculator
Estimate pollutant load from site using Simple Method
2. Apply % Pollutant Removal to estimate annual pollutant load reduction
Pollutant Load Reduction = x
y
Total
% Pollutant
Removal
Annual Pollutant Load
Notes: This was confusing for us. Maybe just make the last point a #3. It feels like the third step in the process

## Slide 52: Questions on annual pollutant removal calculations?

## Slide 53: MIDS Calculator Other Important Notes and Features

## Slide 54: Calculator versus model
MIDS calculator does reasonably good job estimating and tracking volume and pollutant load reductions from common LID best practices
Volume reductions and pollutant load reductions based on detailed modeling and/or literature review
MIDS calculator is not a predictive model
Notes: Allows up to 10

## Slide 55: Does the MIDS calculator handle BMPs in series?
Yes, calculator allows for tracking volume and pollutant removal in treatment train
  Discharge from BMPs can be routed to downstream BMPs
  Calculator allows up to ten of each BMP type
  TP, DP, and TSS tracked throughout BMP treatment train
Treatment train computations not as robust as those in common water quality models
Notes: Allows up to 10

## Slide 56: How does MIDS calculator compare to the EPA calculator?
EPA calculator
Uses SWMM methodology to calculate runoff volumes and reductions
Does not allow multiple soil types
Does not allow multiple BMPs of one type
Only includes volume reduction BMPs. Does not include swales.
Cannot be used to calculate MIDS performance goal requirement or conformance

## Slide 57: How does MIDS calculator compare to common water quality models?
P8/WinSLAMM
More sophisticated runoff prediction
More sophisticated computations of pollutant build-up and wash-off (vary by soil type, land use, precipitation events)
More sophisticated BMP effectiveness simulation

## Slide 58: Results comparison using Exercise 1
 | Percent of Performance Goal Achieved (1.1 inches off impervious surfaces) | Percent Annual Volume Reduction | Percent Annual TP reduction | Percent Annual TSS reduction
MIDS Calculator | 86% | 87% | 87% | 87%
EPA Calculator | N/A | 91% | N/A | N/A
P8* | N/A | 86% | 90% | 97%
WinSLAMM* | N/A | 81% | 71% | 79%
*Modeling conducted 1955 – 2004. Took out super storm of July 23-24, 1987.

## Slide 59: Questions?