## Slide 1
Sarah Hobbie, Dept. of Ecology, Evolution & Behavior, University of Minnesota
Trees as sources of phosphorus to stormwater
Notes: On your own.

## Slide 2
EROSION,
OVERLAND FLOW
LITTERFALL, THROUGHFALL
ATMOSPHERIC DEPOSITION
Potential sources of P to stormwater
Notes: Figure XX. Sources of nutrients (N and P) to stormwater and urban lakes. Atmospheric deposition, lawn fertilizer, and pet waste contribute nutrients to yards and boulevards that can move into streets through erosion, runoff, and litterfall comprising flowers and seeds in spring and leaf litter in autumn. Atmospheric deposition directly to the street and soil erosion contribute additional nutrients to streets. Nutrients in the street move into stormwater(and ultimately into lakes) during rain events and snowmelt, both in solid forms (e.g., as litter fragments) and dissolved forms (e.g., after decomposing bacteria and fungi solubilize nutrients contained in dead leaves in the street). Dead leaves continue to be processed by decomposing microbes in catch basis, storm drains, and stormwater ponds and other best management practices (BMPs), releasing nutrients that can end up in urban lakes. Street sweeping removes nutrient delivered to the street in litterfall and erosion, preventing them from ever reaching urban waters.

## Slide 3: Outline
Phosphorus in tree litterfall
Litterfall contributions to P in street sweepings
Contribution of litterfall P to stormwater P Loading

## Slide 5
Nucleic acids
Phospholipids
Phytate
Orthophosphate
= Bioavailable P

## Slide 6
litterfall

## Slide 7
Spring
Summer
Fall

## Slide 8: Litterfall contributions to P in street sweepings

## Slide 9
MSRC Street Sweeping Study

## Slide 11
City | Study Years | No. routes | Route types | Canopy Cover (%) | Frequency (d) | Sweeper Type | Sweeping Period
Forest Lake | 2019 | 14 | Residential | 1-17 | 14-35 | Regen | Apr-Oct
Mpls | 2019 | 6 | Prkwys, residential, downtown | 0.75-37.5 | 29.2-35.5 | Regen + Mechan | June-Nov
Prior Lake | 2010-2012 | 9 | Residential | 0.1-19.3 | 9.8-37.5 | Regen | Year-round
Roseville | 2019 | 4 | Residential | 13.7-19.6 | 65.3-73.3 | Regen + Mechan | Apr-Nov
Shoreview | 2019 | 7 | Residential | 9.5-22.5 | 45.8-145 | Regen + Mechan | March-Nov

## Slide 12
Soluble | Fines (<2mm) | Coarse Organics (≥2mm) | Rocks
TP, TN, TOC
TS, TP, TN, TC, OM
% moisture
x4
Minneapolis
Roseville
Load wet mass

## Slide 13
Soluble | Fines (<2mm) | Coarse Organics (≥2mm) | Rocks
TP, TN, TOC
TS, TP, TN, TC, OM
% moisture
x4
Minneapolis
Roseville
Load wet mass
Data used in credit calculator

## Slide 14
Litterfall has high P concentrations
Coarse material
Fine sediments

## Slide 15
Litter contributes a high fraction of P to sweepings in fall
Percent of P in sweepings from coarse fraction

## Slide 16
Total P Recovered in Sweepings is Highest where Canopy Cover is High

## Slide 17: Contribution of litterfall P to stormwater P loading

## Slide 18
WCD
Canopy Cover Study
Janke et al. 2017. Environmental Science & Technology

## Slide 19
Chart: 
| 0.29893319448595301 | 0.27366932089360102 | 0.19839965488740899 | 0.224943820913172 | 0.29358002562380697 | 0.23566473683783801 | 0.35585698435990099 | 0.306937796361272 | 0.44702284583558199 | 4.17829398898861E-2 | 1.16224078472456E-2 | 1.3521684737281101E-3 | 2.3907104691035599E-2 | 0.34498914357483301 | 0.21297728648946801 | 0.21616277852012
TP | 0.39429 | 0.41166 | 0.27721 | 0.34628 | 0.42031 | 0.42011 | 0.41107 | 0.26689 | 0.52426 | 0.2498 | 0.15128 | 0.24476 | 0.22444 | 0.47226 | 0.36766 | 0.3082
Across 16 watersheds, stormwater P concentrations increase with canopy cover
Janke et al. 2017. Environmental Science & Technology

## Slide 20: Within one watershed, across seasons, stormwater P matches tree phenology
Finlay et al. in prep.
Total phosphorus (mg/L)
Day of Year
Arlington-Hamline Underground Watershed, Capitol Region Watershed
2007-2016

## Slide 21: How do litterfall P inputs to streets compare to stormwater runoff P yields?

## Slide 22
Urban, residential subwatersheds of the Mississippi River,
Saint Paul, Minnesota
Monitoring
Stations

## Slide 23
Land cover: Kilberg and Bauer 2011

## Slide 24
Ben Janke
Jacques Finlay

## Slide 25
Litterfall P to streets is 37-64% of runoff P

## Slide 26: Conclusions
Trees can contribute substantial bioavailable P to streets and stormwater
Street sweeping should reduce stormwater P loading

## Slide 27
MSRC Street Sweeping Study
University of Minnesota
Sarah Hobbie, Dept. of Ecology, Evolution & Behavior
Larry Baker, Dept. of Bioproducts & Biosystems Engineering
Jacques Finlay, Dept. of Ecology, Evolution & Behavior
Rachel King, PhD student, EEB
Tessa Belo, technician, EEB
Minnesota Pollution Control Agency
Mike Trojan
David Fairbairn
Tetra Tech
Aileen Molloy
Jennifer Olson
Notes: On your own.

## Slide 28
Acknowledgments
Cities of:
  Forest Lake
  Minneapolis
  Prior Lake
  Roseville
  Shoreview
Funding Sources:
  Minnesota Stormwater Research Council
  Environmental Protection Agency
  City of Forest Lake
  Comfort Lake Forest Lake Watershed District