## Slide 1
Trees as sources of nutrient pollution to surface water
Sarah Hobbie
Professor, Dept of Ecology, Evolution & Behavior
University of Minnesota

## Slide 2
Increases in nutrient loading
Reductions in stormwater volume
interception
evapotranspiration
infiltration
litterfall

## Slide 3
Increases in nutrient loading
litterfall

## Slide 6
Trees as Sources of Nutrient Pollution
      Prior Lake Street Sweeping Study
      Canopy Cover Study
      Paired Catchment Study

## Slide 7
Prior Lake Street Sweeping Study
Ross Bintner, Chris Buyarski, Larry Baker, Paula Kalinosky

## Slide 8
Novelty of Prior Lake Study
      Included entire snow-free period
      Included coarse material (litterfall)
      Quantified solids and nutrients in sweepings
      Compiled cost efficiency
      Multi-factor design

## Slide 9: Study Design
Nine Study Routes |  | 
LOW Canopy |  | HIGH Canopy
 | 1X, 2X, 4X/month | 
400 sweepings over 2 years

## Slide 10
Tymco Model 400 Regenerative Air Sweeper

## Slide 11
Soluble | Fines (<2mm) | Coarse Organics (≥2mm) | Rocks
TP, TN, TOC
TS, TP, TN, TC, % Organic
% moisture
x4
Notes: Moisture content of fresh sample and dry mass of each fraction tracked during analysis. Trash content rarely over 1%, but rock content is not. Garbage, ave=0.2 +/- 0.1 % (SD=0.5%), rocks ave=9.4 +/- 0.8% (SD 7.9%). Labs – Soil & Litter TN, TOC – University of Nebraska Ecosystems Analysis Laboratory, all other at U of MN EEB Laboratories.

## Slide 12
Coarse organics (i.e., litterfall) are high fraction of total dry solids, P, and N, especially in autumn
P. Kalinosky MS Thesis
Contribution of coarse organics
(% of total sweeper load)

## Slide 13
Note scale difference
10-fold more material coming into high-canopy streets

## Slide 14: How do litterfall nutrient inputs to streets compare to stormwater runoff nutrient yields?

## Slide 15
Urban, residential subwatersheds of the Mississippi River,
Saint Paul, Minnesota
Monitoring
Stations

## Slide 16
Land cover: Kilberg and Bauer 2011

## Slide 17
Ben Janke
Jacques Finlay

## Slide 18
Litterfall P to streets is 37-64% of runoff P

## Slide 19
WCD
Canopy Cover Study
Ben Janke, Jacques Finlay
Notes: 5 watershed management organizations
16 sites selected based on availability of monitoring data

## Slide 20
Chart: Fractional Tree Canopy over Streets
| 0.29893319448595301 | 0.27366932089360102 | 0.19839965488740899 | 0.224943820913172 | 0.29358002562380697 | 0.23566473683783801 | 0.35585698435990099 | 0.306937796361272 | 0.44702284583558199 | 4.17829398898861E-2 | 1.16224078472456E-2 | 1.3521684737281101E-3 | 2.3907104691035599E-2 | 0.34498914357483301 | 0.21297728648946801 | 0.21616277852012
TP | 0.39429 | 0.41166 | 0.27721 | 0.34628 | 0.42031 | 0.42011 | 0.41107 | 0.26689 | 0.52426 | 0.2498 | 0.15128 | 0.24476 | 0.22444 | 0.47226 | 0.36766 | 0.3082
TN | 2.7365 | 2.5168 | 2.0928 | 2.0707 | 2.3906 | 2.5144 | 2.6227 | 2.0978 | 3.0272 | 2.0749 | 1.757 | 2.4077 | 2.115 | 2.917 | 2.7915 | 2.7219
Across 16 watersheds, stormwater N and P concentrations increase with canopy cover
Janke et al. 2017. Environmental Science & Technology
Notes: No trend in Nox, NH4, or TSS vs street canopy
SRP conc is also significant, and is small portion of TP (~19%)
Regressions with metrics of near-street canopy (buffered roads) produced slightly weaker correlations – big boulevard trees important
Elevated well above rainfall nutrient levels

## Slide 21
Higher tree canopy increases P yields except at low street density
Janke et al. 2017

## Slide 23: Within one watershed, stormwater P matches tree phenology across the seasons
Chart: Stormwater P (mg/L)
Snowmelt
Leaf Out
Leaf Drop
Finlay et al. in prep.
5-year average

## Slide 24
WCD
Paired Catchment Study, Madison, WI
Bill Selbig, USGS, Middleton, WI
Test Catchment: weekly sweeping and leaf removal, Apr-Nov
Control Catchment
17% canopy cover over streets
Notes: 5 watershed management organizations
18 sites selected based on availability of monitoring data

## Slide 25: Treated (swept) catchment has lower runoff P concentrations than control (unswept) catchment
Selbig 2016 Science of the Total Environment

## Slide 26: Treated (swept) catchment has lower runoff P yield
Selbig 2016 Science of the Total Environment
Treatment
(weekly sweeping and leaf removal, Apr-Nov)
Control
(no street sweeping
or leaf removal)

## Slide 27
Solutions:
      Municipal
      Neighborhood
      Individual

## Slide 28
Solutions:
      Municipal: Enhanced Street Sweeping
      Neighborhood
      Individual

## Slide 29
Street Sweeping Calculator Tool
for Public Works & Streets Departments
Enables user to estimate cost and mass of solids and nutrients removed in user-defined sweeping scenarios.
Typical questions:
  1. How much solids and P can I remove for a given budget?
  2. What is the lowest cost to achieve a specific P load reduction goal?

## Slide 31
Example of output from Street Sweeping Calculator Tool
Sample application #1:
What is the lowest cost to remove 35 lb P/yr? Scenario #10
Sample application #2:
What is the most P that can be removed for $2,000? Scenario #6
Route: 10 curb-miles; 20% canopy cover

## Slide 32
https://stormwater.pca.state.mn.us/index.php?title=Street_sweeping_for_trees

## Slide 33
https://stormwater.pca.state.mn.us/index.php?title=Methods_for_calculating_pollutant_reductions_for_street_sweeping

## Slide 34
Chart: Month
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
L4 | 59.7978 | 135.486 | 291.9241 | 371.3393 | 433.2703 | 641.5865 | 468.4593 | 576.1066 | 390.4869 | 484.5152 | 474.2992
H2 | 300.7817 | 86.5669 | 68.4536 | 116.5901 | 112.9717 | 303.6941 | 424.5831 | 147.1383 | 41.4415 | 96.6393 | 480.0382
In high canopy areas, P can be recovered for
less than $100/lb

## Slide 35: Crediting for P Recovery
Five-Fold Cross-Validation for Simple Prediction Measurements | P (lb) | % error
Measured Recovered Phosphorus | 505 | 
Estimate based on measured: |  | 
Curb-miles Swept (predicted recovery) | 525 | (+4.0%)
Fresh Load (lb) | 524 | (+3.7%)
Dry Load (lb) | 516 | (+2.1%)
Notes: Soil P = year 1 and 2 combined, ave = 0.106 , med = 0.08 (H-F)
From random ½ data set, ave=0.107 , med = 0.117.
M-Su, combined, ave = 0.078, med = 0.067
From random, Ave =0.067, med = 0.079
In 7 of 13 metric the median soil Pcame out high in the random assignment, in the full data set 2 of 13 times. (litter P 1 X compared to none.)
260 is error of +25%

## Slide 36: Typical twice/year sweeping only removes 8% of litterfall P inputs to streets

## Slide 38
Phenology

## Slide 40
Sept 7
Oct 2
Oct 27
Citizen scientist phenology data vs. street sweeping, 2013

## Slide 41
Pros: | Cons:
Cost-effective if targeted appropriately | Hard to time
Reduces solids loading downstream & BMP maintenance needs | Requires capital investment
 | Inconvenient for residents
      Municipal: Enhanced Street Sweeping

## Slide 42
Solutions:
      Municipal: Enhanced Street Sweeping
      Neighborhood: Coordinated Leaf Removal
      Individual

## Slide 43
Como Active Citizen Network
Janna Caywood, Lindsay Schwantes, Jessica Bromelkamp
Photos courtesy of Janna Caywood
Notes: Phenology research has informed neighborhood leaf pickup events

## Slide 44
Lessons learned:
      Central management is unsustainable
      Shift from top-down management to network organizing
      Shift from educating to inviting
http://www.capitolregionwd.org/wp-content/uploads/2012/09/Final_Community-Led-Cleanup-Report_Model.pdf

## Slide 45
Pros: | Cons:
Cost-effective | Hard to control
Nimble | Participant fatigue
Engages citizens | Scalable?
      Neighborhood: Coordinated Leaf Removal

## Slide 46
Solutions:
      Municipal: Enhanced Street Sweeping
      Neighborhood: Coordinated Leaf Removal
      Individual: Adopt-a-Drain Programs

## Slide 47
www.capitolregionwd.org
Metro Watershed Partners
Notes: In a more formal way – influence others by creating new neighborhood norms.

## Slide 48
Pros: | Cons:
Cost-effective | Hard to control
Nimble | Hard to assure quality
Engages citizens | Participant fatigue
 | Scalable?
      Individual: Adopt-a-Drain

## Slide 49
Research needs:
      Barriers to enhanced street sweeping
      Mechanisms for crediting P removal
      Cost-effectiveness of street sweeping vs. downstream BMP maintenance
      Extension of Prior Lake study to high-canopy (>20%) neighborhoods
      Effectiveness of neighborhood/individual efforts

## Slide 50
Conclusion:
      Enhanced street sweeping can be effective tool for improving water quality if implemented appropriately
      Neighborhood and individual efforts likely effective if sustained, implemented at scale