## Slide 1
  Clean all sumps/HDS spring & fall
  Priority sumps: 3 times annually
  Summer cleaning based on inspections, budget & weather
  Maintenance timing
  Isolator/Maintenance Row Maintenance Frequency
Sump Maintenance Frequency

## Slide 2
Sump Inspection & Maintenance Documentation
Sump Maintenance By | Avg. Staff Hrs./Sump | Cost Per Each Sump Cleaning
Contract Services (Nelson’s) | 1.10 Hrs. | $140 each
*Average last 3 years. ~375 cleanings per year

## Slide 4
Maintenance Considerations
  Water Management & Decant Water Disposal
    Sanitary Sewer
    Wastewater Facility
    Surface filter area
    Sump pump out
    Other?

## Slide 5
Maintenance Considerations
  Solids Disposal - Requirements?
    Contained Area
    Reuse
    Landfill

## Slide 6: Landfill Disposal Requirements
Toxicity Characteristic Leaching Procedure (TCLP) analysis for 8 RCRA metals: Arsenic, Barium Cadmium, Lead, Mercury, Selenium, Silver.
DRO & Paint Filter Tests

## Slide 12: Pond Pre-Treatment
It is Highly Recommended that each pond have a sediment forebay or equivalent upstream pre-treatment (non-pond BMPs may serve as pre-treatment)
MIDS Design Level 3 Pond (TP = 60%)
Meets all design requirements for Levels 1, 2, 3.
Wet extended detention or multi-cell system
Sediment forebay at all major inflows
Flow path length to pond width ratio 3:1 to 10:1
WQV (flood pool volume) > 1.5 inch of impervious area